## Slide 1: ENHANCING CONTROL IN MICROGRIDS WITH SIMULINK AND OPC: A METHODOLOGY TO BOOST RESEARCHERS AND STUDENTS’ SKILLS
Authors:
Enrico Elio De Tuglie, Luigi Pio Savastio, Giulia Amato, Giovanni Maulà and Arya Abdollahi
Dept. Electrical and Information Engineering, Polytechnic University of Bari
The Learning Ideas Conference 2025
June 11-13 2025

## Slide 2: MAIN AIM
The aim of this work is to provide a comprehensive overview of the use of the OPC protocol in the integration between MATLAB/Simulink and PLC for real-time applications.
Researchers and students gain skills in:
Industrial automation
Smart energy management
Comunication protocols
Monitoring system
Management system with SCADA
Polytechnic University of Bari
De Tuglie et al.

## Slide 3: MICROGRID IN PRINCE LAB
Polytechnic University of Bari
De Tuglie et al.
The microgrid includes:
Cogenerator
Microturbine
Photovoltaic
Wind turbine simulator
BESS
Programmable Loads
V2G System
FOR THIS WORK WE CONSIDER ALSO COGENERATOR AND PROGRAMMABLE LOAD

## Slide 4: MICROGRID’S SYNOPTIC
Polytechnic University of Bari
De Tuglie et al.

## Slide 5: MICROGRID IN PRINCE LAB
Polytechnic University of Bari
De Tuglie et al.
The microgrid’s architecture:
Field level: managed by the PLCs installed on ech field device
Operation level: optimal management and safety
External systems Optimization Level: the students can implement alternative control logic interacting with the field control system

## Slide 6: SIMULINK PROGRAMMING
Polytechnic University of Bari
De Tuglie et al.
Layout:
Client Workstation: used to develop the Simulink Model
OPC GateWay Interface: enables data exchange between industrial devices and management software using the OPC protocol
OPC Server: sends commands to the PLC and receives data for the management system

## Slide 7: OFFLINE SIMULINK MODEL
Polytechnic University of Bari
De Tuglie et al.
This model represents the digital twin of the real generator and load in microgrid:
Cogenerator is represented by a transfer fuction provided by system identification toolbox.
PI controller to closed loop action. This is limitated by upper and lower limits of cogenerator that correspond to 0 and 60 kW
P_Load is a vector of real negative electric load
SP_TL is the setpoint of TieLine that is set equal to 0

## Slide 8: COGENERATOR’S SYNOPTIC
Polytechnic University of Bari
De Tuglie et al.

## Slide 9: CHP TRANSFER FUNCTION IDENTIFICATION
Polytechnic University of Bari
De Tuglie et al.
This toolbox allows users to:
Interact with the real cogenerator and define setpoints;
Record the system’s response and upload the resulting data;
Automatically derive the transfer function from the uploaded data.

## Slide 10: PI TUNING
Polytechnic University of Bari
De Tuglie et al.
Once the transfer function is obtained, it is possible to tune the PI controller using the 'Tune' function and update the PI block. This step is crucial for building the online model that enables interaction with real machines.

## Slide 11: REAL TIME CONTROL
Polytechnic University of Bari
De Tuglie et al.
The simulated transfer function are replaced by OPC tag in order to communicate with the real machine
The actual process signals are read in real time via OPC
The model continues to operate as a real time controller, directly interfacing with the hardware

## Slide 12: REsults
Polytechnic University of Bari
De Tuglie et al.
This figure represents the real system with the control implemented.
Cogenerator active power
TieLine active power
Programmable load active power
This control must guarantee:

## Slide 13: COLLABORATION VS COMPETITION IN TASK EXECUTION
Polytechnic University of Bari
De Tuglie et al.
The control room of the test facility
CHP identification |  |  | 
Group | Number of students | Average execution time | Variance
Group A | 5 | 25 minutes | 10 minutes
Group B | 5 | 15 minutes | 10 minutes
Group C | 4 | 20 minutes | 10 minutes
Group D | 2 | 20 minutes | 10 minutes
PI Tuning |  |  | 
Group A | 5 | 30 minutes | 15 minutes
Group B | 5 | 20 minutes | 15 minutes
Group C | 4 | 25 minutes | 15 minutes
Group D | 2 | 20 minutes | 10 minutes
Real time Control |  |  | 
Group A | 5 | 25 minutes | 20 minutes
Group B | 5 | 15 minutes | 10 minutes
Group C | 4 | 25 minutes | 20 minutes
Group D | 2 | 15 minutes | 10 minutes
Students response per phase
Students were divided into groups to analyze how collaboration and competition affect task execution, focusing on completion time and coordination;
Results showed that larger groups completed task faster but with greater variability, indicating uneven partecipation and task distribution;
Smaller or well coordinated groups were more consistent, though generally slower, highlighting the importance of balanced teamwork for efficiency

## Slide 14: CONCLUSION & LEARNING OPPORTUNITIES
Polytechnic University of Bari
De Tuglie et al.
Seamless Integration Experience: Students and researchers learn to transfer control logic from MATLAB/Simulink to SCADA using OPC, simplifying the management of complex energy systems.
Real Time Microgrid Control: Practical application in the PrInCE Microgrid allows learners to manage a cogenerator for demand balancing and reduced grid reliance.
Collaborative Learning & Innovation: The platform fosters teamwork, competition, and innovation, preparing students with industry relevant, real world automation and energy management skills.

## Slide 15
THANKS FOR YOUR ATTENTION!